## Slide 1: Coordinate Transformations
LLA, ECEF, LTP, Camera Coordinate and Image Coordinate

## Slide 2
World Geodetic System
A unified geodetic system for the whole world. It describes earth as a spheroidal model.
The latest revision is WGS 84 (aka WGS 1984, EPSG:4326), established by US Department of Defense in 1984 and last revised in 2004, now being used in Global Positioning System (GPS).
WGS defines several earth parameters: polar radius, equatorial radius, mass of earth, gravitational constant, rotation rate, etc..
In this system, we use latitude, longitude and altitude to locating.
Notes: A unified geodetic system for the whole world became essential in the 1950s for several reasons:
International space science and the beginning of astronautics.
The lack of inter-continental geodetic information.
The inability of the large geodetic systems, such as European Datum (ED50), North American Datum (NAD), and Tokyo Datum (TD), to provide a worldwide geo-data basis
Need for global maps for navigation, aviation, and geography.
Western Cold War preparedness necessitated a standardized, NATO-wide geospatial reference system, in accordance with the NATO Standardization Agreement

## Slide 3
World Geodetic System – Earth Model
Image@wiki
Polar Radius = 6356752.3142 m
Equatorial Radius = 6378137 m

## Slide 4
World Geodetic System – Latitude and Longitude
λ = longitude
Φ = geodetic latitude
Φ = geocentric latitude 
The flattening of earth
~= 1/298

## Slide 5
World Geodetic System – Latitude and Longitude
Equator
Prime Meridian
Latitude +90
Longitude -180

## Slide 6
World Geodetic System –Altitude
Earth Spheroidal Surface
Terrain Surface
Altitude
Geodetic Latitude

## Slide 7
Earth-Centered, Earth-Fixed (ECEF)
A unified geodetic Cartesian coordinate system.
Intermediate step in converting velocities from WGS coordinate to the local tangent coordinate system.
Its "z-axis" is aligned parallel to the direction of the Conventional Terrestrial Pole (CTP).
Its "x-axis" is the intersection of the WGS84 Reference Meridian Plane and the plane of the CTP Equator.

## Slide 8
Local Tangent Plane (LTP)
A local Cartesian coordinate system with a given origin.
Also called North East Down (NED), North East Up (NEU), Up North East (UNE), etc..
Intermediate step in converting velocities from WGS coordinate to the camera coordinate system.

## Slide 9
Camera Coordinate
A local Cartesian coordinate system, origin is camera center.
Intermediate step in converting velocities from WGS coordinate to the image coordinate system.

## Slide 10
Coordinate Transformations
LLA  ECEF  ENU  Camera Coordinate  Image Coordinate

## Slide 11
Coordinate Transformations: LLA  ECEF
Calculate ellipsoid flattening f.
Calculate eccentricity e.
Calculate the distance N from the surface to z- axis along ellipsoid normal as a function of 𝛷 (geodetic latitude):
The ECEF coordinates X, Y and Z can be calculated from:
revision

## Slide 12
Coordinate Transformations: LLA  ECEF

## Slide 13
Coordinate Transformations: ECEF  ENU
With given origin , the location of in East North Up Coordinate is:
Where R is the rotation matrix:
So the whole transformation is:
revision

## Slide 14
Coordinate Transformations: ECEF  ENU

## Slide 15
Coordinate Transformations: ENU  Camera Coordinate
When our vehicle captures image, it also records camera unit quaternion , the orthogonal matrix is:
With , in camera coordinate is:
revision

## Slide 16
Coordinate Transformations: Camera Coordinate  Image Coordinate
We use “cube” system to present 6 images around camera. In this cube, each face image has field of view (FOV) of 90 degrees and aspect ratio equals 1.
Revision: Y axis here is heading towards ground, it should be a right hand system

## Slide 17
Coordinate Transformations: Camera Coordinate  Image Coordinate
Front
Left
Right
Back
Top
Bottom

## Slide 18
Coordinate Transformations: Camera Coordinate  Image Coordinate
For example, given in camera coordinate, if z>0, z>|x| and z>|y|, then this point belongs to “front” face.
The pixel which this point projects on front cube image with resolution is:
Notice that image coordinate is X-Y-reversed with camera coordinate.

## Slide 19
Project: coordinate transformations
With given point cloud and camera parameters, return the front view of point cloud intensity projection.
Point cloud sample:
45.887308 11.040492 245.240114 40
latitude longitude altitude intensity
Camera parameters:
45.887269, 11.040389, 247.614169, -0.696910, -0.675713, 0.172945, 0.166786
latitude longitude altitude camera quaternion